## Slide 1
VRC-7
AI-Powered Voice Control
for Autonomous Robots
Accent & Noise Robustness in ROS2
Mithila Prabhu-1567111 | Romana Rashid-1428733
Frankfurt University of Applied Sciences M.Eng. in Information Technology
Autonomous Intelligent Systems | Winter 2025/26
Supervised by: Prof. Dr. Peter Nauth

## Slide 2
The Problem
Why existing voice-controlled robots fail in the real world
🔊 Ambient Noise
Hospital/factory environments: 55–70 dB
Equipment alarms, conversations, HVAC
Increases ASR word error rate by 15–40%
Commands get truncated or corrupted
🗣 Accent Diversity
~30% of clinical staff trained abroad (Germany)
ASR models optimised for native phonology
"Turn right" → transcribed as "Törn rät"
Commands silently dropped = no robot action
Research Gap
Existing keyword-based systems are fast but brittle to accents.
LLM-based systems handle accents but exhaust free-tier API limits within 4 minutes.

## Slide 3
VRC-7 System Overview
Three contributions that solve the problem
01
Dual-Layer NLU
Local regex engine handles 85% of commands instantly (0 API calls). Groq LLaMA 3.3 70B invoked only for accent-distorted inputs.
02
Vocabulary-Primed ASR
Groq Whisper with language forcing (language='en') + vocabulary prompt. Raises accented NLU accuracy from 42% → 94%.
03
4-Step Nav Routing
Odometry-based algorithm computing wall-safe waypoints from any position. Eliminates corridor-wall collisions.
📍 Validated using hospital delivery scenario (ICU / Pharmacy / Reception / Ward) as evaluation use case

## Slide 4
System Architecture
Five-module producer-consumer pipeline
Microphone
16 kHz
Energy VAD
RMS>0.02
Silero VAD
p>0.5
Groq Whisper
large-v3-turbo
Layer 1 NLU
Regex <1ms
Layer 2 NLU
LLaMA 3.3 70B
ROS2
/cmd_vel
known?
85%
15%
Gazebo Simulation ↔ TurtleBot3 Burger
/odom
Odometry
/scan
LiDAR 360°
4-Step Nav
Router
← Sensor feedback loop (dashed)
1.5 s
Chunk window
60%
API calls saved by VAD
<1 ms
Layer 1 latency
200–500 ms
Layer 2 latency

## Slide 5
Dual-Layer NLU Architecture
The core innovation of VRC-7
LAYER 1 — Local Regex NLU
30+ compiled regex patterns
Navigation, turns, movement, cardinal, compound
Handles synonyms: "farmasi" = pharmacy, "yellow" = ICU
Sub-millisecond response (<1 ms)
Zero API cost — fully offline
Handles ~85% of all commands
First line of defence — always tried first
unknown
→
LAYER 2 — Groq LLaMA 3.3 70B
Invoked ONLY when Layer 1 fails (~15%)
Interprets semantic INTENT, not keywords
"Törn rät" → turn right (Icelandic mis-decode)
"Donor" → turn around, "farmasi" → pharmacy
temperature=0.0 for deterministic output
85% API call reduction vs full-cloud
4 min → 26 min free-tier operation

## Slide 6
4-Step Room-Exit Navigation Algorithm
Wall-safe routing from any arbitrary position
1
IF inside room (|y| > 2.2m)
Move to target gap x-position (align to corridor entry)
2
Exit through gap
Move to ±1.5m — pass through the corridor entry gap
3
Reach corridor centre
Move to (tx, 0) — navigate along corridor axis
4
Enter target room
Move to (tx, ty) — enter through gap into destination
Hospital World Layout
ICU
(+6,+6)
Pharmacy
(+6,-6)
Reception
(-6,+6)
Ward
(-6,-6)
GAP
GAP
⬤ (0,0)
✓ Correctness proven: every generated path passes exclusively through corridor gap positions — zero wall crossings

## Slide 7
Results: Voice Command Recognition
N=50 trials per condition, 150 total
94%
NLU Accuracy
Accented Speech
+52pp
vs Layer 1
Alone (42%)
73–94%
End-to-End
Accuracy
85%
API Call
Reduction
Condition | Transcription | NLU Accuracy | End-to-End
Quiet (no noise) | 96% | 98% | 94%
Background noise (55 dB) | 82% | 91% | 76%
Accented speech | 78% | 94% | 73%
Key Insight: NLU accuracy (94%) EXCEEDS transcription accuracy (78%) for accented speech. This proves Layer 2 LLaMA 3.3 70B recovers commands that Whisper garbled — semantic inference compensates for imperfect transcription.

## Slide 8
Results: Navigation & API Efficiency
87% overall navigation success · 6.5× API efficiency gain
Navigation Performance
Start | Target | Success | Avg.Time
Centre (0,0) | ICU | 5/5 (100%) | 35 s
Centre (0,0) | Pharmacy | 5/5 (100%) | 37 s
Centre (0,0) | Reception | 5/5 (100%) | 61 s
Centre (0,0) | Ward | 5/5 (100%) | 57 s
Inside room | Other zone | 4/5 (80%) | 62 s
Mid-corridor | Any zone | 3/5 (60%) | 74 s
Overall |  | 26/30 (87%) | 54 s
API Efficiency Comparison
Metric | Full-Cloud | VRC-7
LLM calls/10 cmds | 10 | ~1.5
LLM calls/min | ~20 | ~3
Quota exhaustion | ~4 min | ~26 min
Offline operation | Degraded | Full NLU
System Assessment (0–6 scale)
Nav. accuracy (centre)
Accent robustness (NLU)
Wall collision avoidance
API efficiency
Offline degradation
Weighted mean: 4.8 / 6

## Slide 9
ASR Mitigation Ablation Study
Each mitigation is necessary — all three together are sufficient
No mitigations (raw Whisper + Layer 1)
Transcription: ~23% | NLU: ~20%
20%
+ Language forcing (language='en')
Transcription: ~68% | NLU: 42%
42%
+ Vocabulary priming
Transcription: 78% | NLU: ~55%
55%
+ Layer 2 LLaMA 3.3 70B (full VRC-7)
Transcription: 78% | NLU: 94%
94%
74 percentage point improvement over no-mitigation baseline | All three mitigations individually necessary

## Slide 10
Challenges & Solutions
Five engineering challenges encountered and resolved
⚠ Challenge:
WSL2 Audio (PaErrorCode -9987)
✓ Solution:
Set PULSE_SERVER env var before sounddevice import
⚠ Challenge:
Groq API Rate Limiting (4 min quota)
✓ Solution:
Dual-layer NLU + VAD cascade → 26 min operation
⚠ Challenge:
Corridor wall collisions
✓ Solution:
4-step routing algorithm — always routes through gaps
⚠ Challenge:
Accent mis-transcription as foreign language
✓ Solution:
language='en' + vocab prompt + LLaMA Layer 2
⚠ Challenge:
TurtleBot3 tipping at 0.9 m/s
✓ Solution:
Speed limited to 0.5 m/s — physics stable, 200+ runs

## Slide 11
Conclusion & Future Work
What VRC-7 Demonstrates
100% navigation success from centre position
94% NLU accuracy for accented speech (+52pp vs baseline)
85% API call reduction → 26 min free-tier operation
Accent robustness and API efficiency are NOT in conflict
Dual-layer architecture generalises to any robot domain
Future Extensions
1
SLAM Navigation
Nav2 + AMCL replaces odometry drift
2
Multilingual Support
German, French, Hindi in LLaMA prompt
3
Local LLM (Ollama)
GGUF 4-bit LLaMA — no API dependency
4
Multi-Robot Fleet
ROS2 namespacing + robot addressing
🔗 github.com/Mprabhu26/turtlebot_vrc | Autonomous Intelligent Systems · Winter 2025/26 · Frankfurt UAS · Prof. Dr. Peter Nauth

## Slide 12
Thank You
Mithila Prabhu & Romana Rashid
Frankfurt University of Applied Sciences
Autonomous Intelligent Systems · Winter 2025/26
Supervised by Prof. Dr. Peter Nauth
github.com/Mprabhu26/turtlebot_vrc